## Slide 1: Susceptibility-weighted imaging (SWI)
Tzu-Wei (Charles) Lee

## Slide 2: Susceptibility-weighted imaging (SWI)
Susceptibility-weighted imaging (SWI) is a technique, which uses tissue magnetic susceptibility differences to generate a unique contrast
Susceptibility-Weighted Imaging: Technical Aspects and Clinical Applications, Part 1
E.M. Haacke, S. Mittal, Z. Wu, J. Neelavalli and Y.-C.N. Cheng
American Journal of Neuroradiology January 2009, 30 (1) 19-30
Notes: Concept

## Slide 3: Susceptibility-weighted imaging (SWI)
Notes: phase : spin thermal relaxation in a voxel , water motion (diffusion, perfusion, tissue deformation) , molecule electron cloud polarization
Magnitude based
Phase image as the contrast enhancement mask
Specifically, the phase images themselves can provide excellent contrast between gray matter (GM) and white matter (WM), iron-laden tissues, venous blood vessels, and other tissues with susceptibilities that are different from the background tissue.
Also, for the first time, projection phase images are shown to demonstrate tissue (vessel) continuity. In this work, the best approach for combining
magnitude and phase images is discussed

## Slide 4: SWI Advantage
Optic nerve well shown
Fat signal saturation simplify
GM & WM more clearly
Susceptibility-Weighted Imaging; Magn Reson Med. 2004 Sep;52(3):612-8.; Haacke EM1, Xu Y, Cheng YC, Reichenbach JR.
magnitude
phase
SWI
SWI(*2)
Notes: One is about optic nerve observation as comparing A & D
Seccond, is about fat saturation that we could fat sat easier on SWI
Thrid one, is SWI can have the greater contrast on GM & WM

## Slide 5: SWI Application
Susceptibility-Weighted Imaging: Technical Aspects and Clinical Applications, Part 2
S. Mittal,Z. Wu,J. Neelavalli, E.M. Haacke
A: FLAIR
B: T1-weighted Image
C: TE=40 magenitude Image
D: SWI phase Image
A patient who had sudden onset of aphasia and right paresthesias 5 years earlier and who partially recovered neurologic function after treatment of the acute stroke
hemorrhage
Notes: Clinical Application
To date, SWI has had most of its clinical applications in the neuroimaging arena
veins
Hemorrhage
Including imaging cartilage, imaging calcium in atherosclerosis, imaging breast, and liver hemochromatosis.

## Slide 6: Susceptibility
Observing susceptibility inhomogeneous
  From >> magnetic field inhomogeneous
by viewing as B0 map
  From >> processing different (susceptibility)
by determine by particle property
http://mriquestions.com/what-is-spin.html
Notes: Briefly show the principle of SWI
So what is susceptibility ~ susceptibility is a particle property about the spin that affect on magnetic Field

## Slide 7: Susceptibility to Magnetic Field
Signal we acquired are from processing
Particles spins in a material orient in the same direction as the magnetic field is called paramagnetism
Particles oppose the applied field; this is called diamagnetism
https://mri-q.com/causes-of-susceptibility.html
https://radiopaedia.org/articles/paramagnetism
Paramagnetism
Dimagnetism
Notes: Different matter will create Different magnetism one is para and another is dia

## Slide 8: Spin to data
https://betterexplained.com/wp-content/uploads/2016/12/circle-two-sine-waves.gif
http://mriquestions.com/real-v-imaginary.html
Quadrature(Q) = “imaginary” part
In phase (I) = “real” part
Total
Two channels receive two signals
Notes: We acquired data from two channels that we could define one is called the imaginary part
And another wiould called the real part

## Slide 9: Image Data
Magnetic Image
Phase Image
http://mriquestions.com/real-v-imaginary.html
Notes: Polar coordinate system
phase Image is constructed from the phase from the blue vector to the real part
Phase images contain information about the background magnetic field

## Slide 10: SWI process
Phase Image
High-pass filtered phase
there is high phase signal only
Phase mask
Notes: From phase Img to create a high pass filtered phase
then make the phase mask from the high pass phase

## Slide 11: Phase Mask
High-pass Phase
As we know phase data is around :
Susceptibility Weighted Imaging (SWI) E. Mark Haacke,1-4* Yingbiao Xu,1,2 Yu-Chung N. Cheng,1 and Ju¨ rgen R. Reichenbach
Magnetic Resonance in Medicine 52:612– 618 (2004)
G(x) =
F(x) =
Phase mask
Negative mask
Positive mask
High pass filter
Notes: formula
These corrected phase images were then set between zero and unity to get the phase mask.
If the contrast we wont to enhance is between from negative pi to zero , then we could apply the upper formula, on the other hand
If the contrast we wont to
Reduce
lower

## Slide 12: SWI process
Magnitude Image
Phase mask
SWI
^5
Notes: A three-dimensional multiple-gradient-echo (MGE) imaging sequence was implemented.
The corrected phase images were set between zero and unity to get the phase mask (2).
The magnitude images were multiplied with the phase masks five times to enhance the visibility of the venous structures (2).

## Slide 13: SWI tech combine
Use mIP (Minimum Intensity Projection) to enhance veins and hemorrhage
https://en.wikibooks.org/wiki/Basic_Physics_of_Nuclear_Medicine/Three-Dimensional_Visualization_Techniques#/media/File:IntProjs3.jpg
Notes: To visual vessel & hemorrhage in a volume
We use mIP as a contrast enhance tech
mIP is finding the manimum of different slice to create a new Image that has a lot information of different slice darkest matter
maybe vessel or hemorrhage or something elses

## Slide 14: SWI mIP
Mag
SWI
+
mIP*1

## Slide 15: SWI mIP
Mag
SWI
+
mIP*2

## Slide 16: SWI mIP
Mag
SWI
+
mIP*3

## Slide 17: SWI mIP
Mag
SWI
+
mIP*4

## Slide 18: SWI mIP
Mag
SWI
+
mIP*5

## Slide 19: Matlab code

## Slide 20: A new SWI (combined SWI and SWAN) technique in visualizing nigrosome 1 of the substantia nigra
My Project
Tzu-Wei (Charles) Lee
Notes: I suggest that Multi-echo-gradient-echo pulse sequence is a technique that better than the conventional single pulse one.
And focus on single specific clinic sign and

## Slide 21: Swallow Tail in Parkinson’s Disease
Swallow tail
https://jis.gov.jm/information/symbols/jamaican-national-bird-the-doctor-bird/
Normal people show swallow sign
Parkinson’s Disease patient show no swallow sign
Nigrosome1 (melanin)
Substantia nigra
Notes: Section of midbrain where a portion of the substantia nigra is visible
Swallowtail appearance is a new or not that new and easy applicable MRI diagnostic tool for nigral degeneration in PD

## Slide 22: Swallow Tail Sign
1 red nucleus
2 midbrain tegmentum
3 aqueduct
4 periaqueductalgrey
5 medial leminiscus
6 nigrosome-1
7 substantia nigra
8 cerebral peduncle
9 mammillary body
The ‘Swallow Tail’ Appearance of the Healthy Nigrosome– A New Accurate Test of Parkinson’s Disease: A Case- Control and Retrospective Cross-Sectional MRI Study at 3T
Stefan T. Schwarz1*, Mohammed Afzal2, Paul S. Morgan3, Nin Bajaj4, Penny A. Gowland5,
Dorothee P. Auer1
10 inter-peduncular fossa
11 optic radiation
12 3rd ventricle
13 temporal lobe
14 cerebellum
15 frontal lobe.
Notes: Anatomy

## Slide 23: Swallow Tail in Parkinson’s Disease
Healthy Subject
PD Patient
3T Siemens PRISMA
Notes: Section of midbrain where a portion of the substantia nigra is visible

## Slide 24
New Tech
Routine SWI
Subject 01
Notes: sinuses

## Slide 25
New Tech
Routine SWI
Subject 01

## Slide 26
New Tech
Routine SWI
Subject 01
Notes: 你看frontal sinus和耳洞的susceptibility artifact用新的技術都補回來了
Cochlea

## Slide 27
New Tech
Routine SWI
Subject 02

## Slide 28
New Tech
Routine SWI
Subject 02

## Slide 29
New Tech
Routine SWI
Subject 02

## Slide 30: Result – Swallow Tail sign
Notes: section of midbrain where a portion of the substantia nigra is visible
The recent advance in MR imaging has shown the potential role of susceptibility-weighted imaging (SWI) in visualizing the nigrosome1, which is a known marker for Parkinson disease(1).
Multi-echo-gradient-echo pulse sequence is a technique which can provide the higher image quality by the weighted sum of the images from different echo times and the quantitative measures of susceptibility using phase information. In this work, we used a hybrid technique by combing magnitude and phase images from different echo times to assess its potential in the depiction of the nigrosome1.
The new hybrid technique of susceptibility-weighted imaging (SWInew) combined magnitude and the filtered phase images from different echo times.
The contrast-to-noise ratio (CNR) was calculated focusing on the ratio of signal intensity from the nigrosome1 to its surrounding area in the substantia nigra.
We compared the CNR between the new hybrid technique and the conventional SWI and T2* map in 22 normal subjects.

## Slide 31: Swallow Tail sign Boundary
Fuzzy cluster mean (FCM)
To segment the Nigrosome1 & Substantia nigra
Distance
+
Signal intensity
1
Find minimum
Notes: Section of midbrain where a portion of the substantia nigra is visible
cluster analysis

## Slide 32: Contrast to Noise Ratio(CNR)
CNR
  To quantify the signal from swallowtail sign
Sum Signal intensity of Substantia nigra
Sum Signal intensity of Nigrosome1
Notes: Section of midbrain where a portion of the substantia nigra is visible
Statistics
Matlab

## Slide 33: Results – CNRs
Technique | mean
Left_CNR_swi_new | 28.2710.26%
Right_CNR_swi_new | 25.678.07%
Left_CNR_SWI | 22.6210.00%
Right_CNR_SWI | 20.50%
Left_T2* | 41.76 14.99%
Right_T2* | 37.09%
Technique | mean
Left_CNR_swi_new | 
Right_CNR_swi_new | 
Left_CNR_SWI | 
Right_CNR_SWI | 
Left_T2* | 
Right_T2* | 
Notes: Section of midbrain where a portion of the substantia nigra is visible

## Slide 34: Conclusion
The enhanced nigrosome1 in the T2* map might be attributed to its long T2 value
Notes: Nigrosome1 melanin

## Slide 35: Future Work
Quantitative Susceptibility Mapping (QSM)
Questions or Suggestions
Notes: Section of midbrain where a portion of the substantia nigra is visible

## Slide 36: supplement

## Slide 37: Spin to data
https://betterexplained.com/wp-content/uploads/2016/12/circle-two-sine-waves.gif
http://mriquestions.com/real-v-imaginary.html
Total
Re
Im

## Slide 38: High Pass Filter Image
Fill in zeros of low freq
K-space
Phase Image
None wrapped Phase
(high-pass filtered phase)

## Slide 39: Multiplication of Mask making
Susceptibility-Weighted Imaging; Magn Reson Med. 2004 Sep;52(3):612-8.; Haacke EM1, Xu Y, Cheng YC, Reichenbach JR.
To acquire best contrast, how many times should we multiply?
CNR & SNR trade off
Notes: Line Graph
The more we multiply the better contrast we get
It is a trade off of CNR ( contrast 2 noise ratio ) & SNR ( signal 2 noise ratio )
The more we multiply, the contrast we get is better, but the SNR is increasing at the same time

## Slide 40: Image compare
Susceptibility-Weighted Imaging: Technical Aspects and Clinical Applications, Part 1; E.M. Haacke, S. Mittal, Z. Wu, J. Neelavalli, Y.-C.N. Cheng
Mag+phase
(unprocessed)
HP phase
SWI
(full-processed)
Notes: Maybe we can see the contrast from the image of the process
Why not just highpass Image or SWI mitiply phase mask*1

## Slide 41: SWI mIP
Susceptibility-Weighted Imaging: Technical Aspects and Clinical Applications, Part 1; E.M. Haacke, S. Mittal, Z. Wu, J. Neelavalli, Y.-C.N. Cheng

## Slide 42: Vessels & Hemorrhage Contrast
Susceptibility-Weighted Imaging; Magn Reson Med. 2004 Sep;52(3):612-8.; Haacke EM1, Xu Y, Cheng YC, Reichenbach JR.
mIP magnitude
mIP SWI
mIP phase
Notes: 出血
hemorrhage